## Slide 1
Alaska Clean Seas
Spill Response Equipment Catalog
2022

## Slide 2
Printing Instructions:
For best results, set to print in color, two-sided, 8 ½ x 11 inch Letter paper. The inserted blank pages will allow each section break to begin on an odd page.

## Slide 3
Membership of ACS

## Slide 4
This page intentionally left blank.

## Slide 5
Introduction
This Manual provides a guide to the location, ownership, type, amount and specifications to North Slope response equipment that Alaska Clean Seas (ACS) utilizes. In 1995, all spill equipment on the North Slope except Alyeska was consolidated, which brought it all into one tracking and maintenance system.
Spill response equipment warehouses, storage yards, and satellite areas are strategically located in each operating field and at two separate locations in Deadhorse. With assistance from ACS Base, field-assigned ACS technicians support the operating area facilities and sites; while the Deadhorse locations are managed by ACS Base personnel.
ACS technicians perform required preventative and routine maintenance activities on both ACS and Member Company dedicated spill response equipment. Equipment repairs beyond the capabilities of ACS technicians are accomplished by mechanics assigned to either ACS Base in Deadhorse/Marine or mechanics at Alpine and Kuparuk. These shops perform complex maintenance tasks and maintain vessels and specialized response equipment. Off-shore marine vessels and equipment are maintained and repaired by Marine mechanics at A4W1. Major equipment modification work and specialized fabrication are also accomplished at these facilities.
Currently, the value of dedicated spill response equipment warehoused under ACS management exceeds $75 million. ACS owns roughly half of this equipment while the Member Companies own the other half. With the exception of repair or maintenance costs, all ACS owned equipment is available to Member Companies at no charge, during a spill response. Member owned equipment is available to all other members under terms and conditions outlined in the North Slope Mutual Aid Agreement.
In summary, ACS maintains a vast amount of equipment located throughout the operating oil fields on the North Slope of Alaska. This manual is intended to assist potential users in understanding ACS spill response equipment and how they might access it for both spill and non-spill related work.
Should there be any questions regarding the equipment, please contact us at (907) 659-2405.

## Slide 6
This page intentionally left blank.

## Slide 7
Table Of Contents
Safety | Section A
Meters | Page 1
Automated External Defibrillators (AEDs) | Page 2
Emergency Locater Beacons (EPIRB) and Global Position Indicating Radio Beacons (GPIRB) | Page 3
Life Rafts | Page 4
Dry Decons | Page 5
Wet Decons | Page 6
Vessels and Accessories | Section B
Agviq | Page 7
Big Dipper | Page 8
Point McIntyre | Page 9
Bay Boats | Page 10
Fireweed and Arctic Rose | Page 11
Deployer and Retriever | Page 12
Island Boats | Page 13
Bullet and Snow White | Page 14
Large Landing Crafts | Page 15
Small Landing Crafts | Page 16
Near-shore Work Boats | Page 17
Airboats | Page 18
Outboards | Page 19
Recovery Equipment | Section C
LORI Brush Skimmers | Page 20
Vikoma Weir Skimmers | Page 21
Foxtail Rope Mop Skimmer | Page 22
I

## Slide 8
Table Of Contents - Continued
Desmi Skimmers (Ocean and Harbor) | Page 23
Disc Skimmers | Page 24
Drum/Brush Skimmers | Page 25
Grooved Drum Skimmer w/Steam Coils and Steam Trailers | Page 26
Crucial Fuzzy Disc Skimmer | Page 27
Crucial Fuzzy Drum Skimmer | Page 28
Lamor Brush Belt Skimmer and Rock Cleaners | Page 29
Skimmer Rope Mops | Page 30
SeaVac Heli-Skimmer | Page 31
Manta Ray Skimmers | Page 32
Vac Units | Page 33
Mini Vac Units | Page 34
Air Power Units | Page 35
Snow Blowers | Page 36
Ice Augers | Page 37
Jackhammers | Page 38
Chainsaws and Ice Trenching Tools | Page 39
Rube Witches | Page 40
Containment | Section D
Delta/River Boom | Page 41
Boom Rudders | Page 42
Boom Handler | Page 43
Shore Seal Boom | Page 44
T-Fence Boom | Page 45
Kepner Boom Reel Packs | Page 46
II

## Slide 9
Table Of Contents - Continued
NOFI Ocean Boom | Page 47
NOFI Harbor Buster | Page 48
Ro-Boom | Page 49
Goodyear Ocean Boom | Page 50
Abasco Harbor Boom | Page 51
Lamor Boom Reel Packs | Page 52
Boom Inflating Blowers | Page 53
Floating Pumps - 1 ½ ” | Page 54
Pipe/Culvert Plugs | Page 55
Water Spray Trailer | Page 56
In-Situ Burn Equipment | Section E
Helitorch Gelled Fuel Mixers | Page 57
Handheld Igniters | Page 58
Fire Boom | Page 59
Helitorches | Page 60
Transfer and Storage | Section F
Barges 125 BBL | Page 61
Barges 249 BBL | Page 62
Barge 650 BBL | Page 63
Viscous Oil Annular Injection Kits | Page 64
Fastank/Fold-A-Tanks | Page 65
Self Rising Tanks | Page 66
Floating Tank | Page 67
Upright Tank | Page 68
Bladders | Page 69
III

## Slide 10
Heavy Oil Pumps | Page 70
Air Diaphragm Pumps 0.5” to 3” | Page 71
Diesel/Hydraulic Diaphragm Pumps 2” and 3” | Page 72
Gas Diaphragm Pumps 3” | Page 73
Diesel/Hydraulic Peristaltic Pumps 2” , 2 ½” and 3” | Page 74
Sykes Univac Diesel Pumps 3” | Page 75
Centrifugal Pumps 2”, 3” and 4” | Page 76
Emergency Dewatering Pumps 2” | Page 77
Logistics Support Equipment | Section G
Centaur 950DT | Page 78
4-Wheelers | Page 79
Kubotas with Tracks | Page 80
Tucker Sno-Cat | Page 81
Bobcat Tool Cat 5600 | Page 82
Snow Machines and Sleds | Page 83
Muck Truck Motorized Wheelbarrow | Page 84
Passenger/Work Vehicles | Page 85
14 Passenger Bus | Page 86
Medium Duty Flatbed | Page 87
Truck Tractors | Page 88
Boom Trucks | Page 89
Mechanics’ Trailers | Page 90
Dump Truck | Page 91
Dempster System Equipped Trucks | Page 92
Skid Steer Loaders | Page 93
Warehouse Fork Lifts | Page 94
IV
Table Of Contents - Continued

## Slide 11
Table Of Contents - Continued
Front End Loaders w/attachments | Page 95
Mobile Command Centers | Page 96
Staging Area Manager Offices | Page 97
Winter Response Vans | Page 98
Tanker Rollover Van | Page 99
Steam Van | Page 100
Warm Up/Break Shacks | Page 101
Portable Shelters | Page 102
Portable Shops | Page 103
Portable Restroom Units | Page 104
Indirect Fired Heaters | Page 105
Under Water Drop Lights | Page 106
Light Plants and Stands | Page 107
Diesel Generators (various) | Page 108
Gas Generators (various) | Page 109
Air Compressors | Page 110
20’ and 40’ Connex | Page 111
Portable Fuel Tanks | Page 112
Communications | Section H
Portable Communications Towers | Page 113
Portable Communications Shelters | Page 114
Handheld Radios | Page 115
Iridium Phones | Page 116
Mobile Radios | Page 117
GPS | Page 118
Gap Fillers | Page 119
Radio Winter Drilling Kits | Page 120
V

## Slide 12
Table Of Contents - Continued
Wildlife | Section I
Pinniped Enclosure | Page 121
Bear Cages | Page 122
Net Launchers | Page 123
Wildlife Kits(capture and hazing) | Page 124
PepperBall Gun | Page 125
12 Gauge Shot Guns | Page 126
Bird Stabilization Center | Page 127
Bird Scare Devices | Page 128
Miscellaneous | Section J
De-Icer Ground Penetrating Radar System | Page 129 Page 130
Hydraulic Power Units (various) | Page 131
MegaSecur Dams | Page 132
MetOcean Spill Tracking Systems | Page 133
Underwater ROV | Page 134
Unmanned Aircraft Systems | Page 135
VI
Abbreviation | Name
ACS | Alaska Clean Seas
CPAI | ConocoPhillps Alaska Inc.
ENI | ENI Alaska
HAK | Hilcorp Alaska
Savant | Savant Alaska
Abbreviations

## Slide 13
Safety
Section A

## Slide 14
This page intentionally left blank.

## Slide 15
Meters |  |  |  | 
Quantity: | 20 Total |  |  | 
Manufacturers: | Draeger, Ex Tech, Fit Check, Gas Clip Technologies, and Rae Systems |  |  | 
Owner(s): | (6) Four Gas, ACS |  | (5) PIDs, ACS | (1) Tube Pump, ACS
 | (1) Sound Meter, ACS |  | (1) CMS, ACS | (1) Fit Check Solo, ACS
 | (1) Light Meter, ACS |  |  | 
 | (1) Six Gas, CPAI |  | (1) PID, CPAI | 
 | (2) Six Gas, HAK |  |  | 
Function: | Air and sound sampling, fit testing and monitoring |  |  | 
1

## Slide 16
Automated External Defibrillators (AEDs) |  |  | 
Quantity: | 6 Total |  | 
Manufacturer: | Cardiac Science and Phillips |  | 
Owner(s): | ACS |  | 
Specifications: | Cardiac Science-9390A, Phillips 861304, and M5066A |  | 
Function: | Emergency first aid. |  | 
2

## Slide 17
Emergency Locator Beacons (EPIRB and GPIRB) |  | 
Quantity: | 15 Total | 
Manufacturer: | ACR Electronics | 
Owner(s): | ACS | 
Specifications: | 406 MHz Satellite, Cat 1, Class 2 | 
Function: | Emergency location of vessels and personnel. | 
3

## Slide 18
Life Rafts |  |  |  | 
Quantity: | 36 Total |  |  | 
Manufacturer: | DBC, Guardian and Viking |  |  | 
Owner(s): | 32 each, ACS 4 each, HAK |  |  | 
Specifications: | 6 each, 4 person 11 each, 6 person |  |  | 
 | 15 each, 10 person 4 each, 6 person, HAK |  |  | 
Function: | Life saving equipment for vessels in distress. |  |  | 
4

## Slide 19
Dry Decons |  |  |  |  |  | 
Quantity: |  | 8 Total |  |  |  | 
Manufacturer: |  | Alchem, Ameri-can, Fruehauf, Hobbs, Union Cointainer Industries, and Wells Cargo |  |  |  | 
Owner(s): |  | 2 each, ACS |  | 2 each, CPAI |  | 
 |  | 4 each HAK |  |  |  | 
Specifications: |  | 20’ to 50’ trailer or connex units |  |  |  | 
Function: |  | Provide dry decon facilities during response operations. |  |  |  | 
Auxiliary Equip: |  | Generator, Tail Roll Truck or Trailer |  |  |  | 
5

## Slide 20
Wet Decons |  |  |  |  | 
Quantity: | 1 Total |  |  |  | 
Manufacturer: | Intercontinental |  |  |  | 
Owner(s): | CPAI |  |  |  | 
Specifications: | These self-contained decontamination units are designed to be hauled with either a Dempster system equipped truck or a pickup truck to a spill response site. |  |  |  | 
Function: | Designed to accommodate either wet or dry decon processes. |  |  |  | 
Auxiliary Equip: | Generator power for Kuparuk unit: HAK equipped with dedicated generator. Transport truck. |  |  |  | 
6

## Slide 21
Vessels and Accessories
Section B

## Slide 22
This page intentionally left blank.

## Slide 23
Agviq |  | 
Quantity: | 1 Total | 
Manufacturer: | Grayling Marine | 
Owner(s): | ACS | 
Specifications: | Draft: 2’ 6” | 
 | Fuel Capacity: 900 gallons | 
 | Twin Lugger, 250 HP each, jets | 
 | Range: 280 NM @ 2300 RPM w/28 HRS operating time | 
 | Cruising Speed: 8 -12 kts | 
 | 55 ft., 45,000 lbs. | 
Function: | Transporting equipment and personnel, boom deployment and skimming activities. | 
7

## Slide 24
Big Dipper |  | 
Quantity: | 1 Total | 
Manufacturer: | Grayling Marine | 
Owner(s): | ACS | 
Specifications: | Draft: 2’6” | 
 | Fuel Capacity: 632 gallons | 
 | Twin CAT, 450 HP each, jets | 
 | Range: 75 NM @ 2400 RPM w/17.5 HRS operating time | 
 | Cruising Speed: 8 -12 kts | 
 | 45 ft., 37,000 lbs. | 
Function: | Transporting equipment and personnel, boom deployment and skimming activities. | 
8

## Slide 25
Point McIntyre |  | 
Quantity: | 1 Total | 
Manufacturer: | Munson | 
Owner(s): | ACS | 
Specifications: | Draft: 2’8” | 
 | Fuel Capacity: 500 Gallons | 
 | Engines: Twin Volvo D13 800HP (Rated 800 BHP @ 2,300 RPM) / Twin Hamilton HJ403 jet drives Persons and Cargo Capacity:12,000 lbs. | 
 | Range: 127 NM @ 2150 RPM w/12 HRS operating time | 
 | Cruising Speed: 22-25 Knots@ 2150 to 2200 RPM | 
 | 48 ft., 45,951 lbs. 16’ beam | 
Function: | Equipment and personnel transport /deploying and towing open ocean containment boom, operating oil skimmers, towing small oil spill response barges. | 
9

## Slide 26
Bay Boats |  | 
Quantity: | 3 Total | 
Manufacturer: | Rozema Boat Works | 
Owner(s): | ACS | 
Specifications: | 1 each, Camden Bay, Gwydyr Bay, and Mikkelsen Bay | 
 | Draft: 3’9” | 
 | Fuel Capacity: 700 gallons | 
 | Twin Lugger, 450 HP each, prop | 
 | Range: 340 NM @ 2,000 RPM w/20 HRS operating time | 
 | Cruising Speed: 17 kts | 
 | 42 ft., 37,000 lbs. | 
Function: | Moving and deploying boom, skimmers, containment barges, and transporting personnel and equipment. The twin engine power supply allows for larger towing capacity and provides increased speed. | 
10

## Slide 27
Fireweed and Arctic Rose |  | 
Quantity: | 2 Total | 
Manufacturer: | Munson | 
Owner(s): | ACS | 
Specifications: | 1 each, Fireweed and Arctic Rose | 
 | Draft: 2’8” | 
 | Fuel Capacity: 650 gallons | 
 | Twin Cummins, 250 HP each, prop | 
 | Range: 456 NM @ 2300 RPM w/38 HRS operating time | 
 | Cruising Speed: 12 kts | 
 | 38 ft., 30,000 lbs. | 
Function: | Transporting equipment and personnel, towing boom and mini-barges for spill response. | 
11

## Slide 28
Deployer and Retriever |  | 
Quantity: | 2 Total | 
Manufacturer: | Munson | 
Owner(s): | ACS | 
Specifications: | Draft: 2’ | 
 | Fuel Capacity: 200 gallons | 
 | Twin Evinrude Outboards, 150 HP each, prop | 
 | Range: 175 NM, 4,000 RPM w/ 7.5 HRS operating time | 
 | Cruising Speed: 23 kts | 
 | 29 ft., 9,000 lbs. | 
Function: | Boom towing, mini-barges, bladders and transport personnel and equipment. | 
12

## Slide 29
Island Boats |  | 
Quantity: | 4 Total | 
Manufacturer: | Rozema Boat Works | 
Owner(s): | HAK | 
Specifications: | 1 each, Karluk Island, Cottle Island, Barter Island and Narwhal Island | 
 | Draft: 3’9” | 
 | Fuel Capacity: 172 gallons | 
 | Single CAT, 300 HP, prop | 
 | Range: 144 NM @ 2,400 RPM w/12 HRS operating time | 
 | Cruising Speed: 8 kts | 
 | 25 ft., 14,800 lbs. | 
Function: | Boom towing and mini-barge operations. | 
13

## Slide 30
Bullet and Snow White |  | 
Quantity: | 2 Total | 
Manufacturer: | Munson | 
Owner(s): | ACS | 
Specifications: | 1 each, Bullet and Snow White | 
 | Draft: 1’6” | 
 | Fuel Capacity: 79 gallons, Bullet | 
 | Fuel Capacity: 147 gallons, Snow White | 
 | Twin Evinrude Outboards, 90 HP each, prop, Bullet Single Chevrolet 350ci inboard, w/Volvo Penta outdrive, Snow White | 
 | Cruising Speed: 20 kts | 
 | 21 ft., 6,000 lbs. | 
Function: | Near-shore operations to include boom towing. | 
14

## Slide 31
Large Landing Crafts |  | 
Quantity: | 4 Total | 
Manufacturer: | Munson, Riddle | 
Owner(s): | 1 each, ACS 1 each, CPAI 2 each, HAK | 
Specifications: | Draft: 20 in. - 2 ft. | 
 | Fuel Capacity: 300 - 400 gallons | 
 | Twin Evinrude 300 Outboards, Twin Yanmar 350 Diesel | 
 | Cruising Speed: 27 - 30 kts | 
 | 34 ft. - 37 ft., 14,100 lbs. – 18,500 lbs. | 
Function: | Transporting equipment, personnel, and boom deployment for near-shore response operations. | 
15

## Slide 32
Small Landing Crafts |  |  |  |  |  |  |  |  |  |  |  | 
Quantity: |  |  |  | 6 Total |  |  |  |  |  |  |  | 
Manufacturer: |  |  |  | Grayling Marine, Munson and Riddle |  |  |  |  |  |  |  | 
Owner(s): |  |  |  | 4 each, ACS |  |  |  | 1 each, CPAI |  |  |  | 
 |  |  |  | 1 each, HAK |  |  |  |  |  |  |  | 
Specifications: |  |  |  | Draft: 1’- 3’ |  |  |  |  |  |  |  | 
 |  |  |  | Fuel Capacity: 60 - 150 gallons |  |  |  |  |  |  |  | 
 |  |  |  | Cruising Speed: 20 - 30 kts |  |  |  |  |  |  |  | 
 |  |  |  | 22 to 32 ft., 2,200 lbs. – 12,000 lbs. |  |  |  |  |  |  |  | 
Function: |  |  |  | Transporting equipment, personnel, and boom deployment for near-shore response operations. |  |  |  |  |  |  |  | 
16

## Slide 33
Near-shore Work Boats |  |  |  |  |  | 
Quantity: | 34 Total |  |  |  |  | 
Manufacturer: | Achilles, Alaska Frontier Fabricators, Aztec, Gregor, Inmar Inflatables, Lowe, Marian, Munson, Phantom, Sea Ark, Riddle, Rozema, Sea Ark, Sea Nymph, SJX, Smokecraft, Valco, and Woolridge |  |  |  |  | 
Owner(s): | 10 each, ACS |  | 16 each, CPAI |  |  | 
 | 1 each, ENI |  | 7 each, HAK |  |  | 
Specifications: | 12’ to 28’ rigid hulled up to 200 HP |  |  |  |  | 
Function: | Containment, recovery and logistical support for near-shore response operations. |  |  |  |  | 
17

## Slide 34
Airboats |  |  |  |  |  |  | 
Quantity: | 33 Total |  |  |  |  |  | 
Manufacturer: | Alumitech, Diamondback, and Husky |  |  |  |  |  | 
Owner(s): | 16 each, ACS | 5 each, CPAI |  |  |  |  | 
 | 12 each, HAK |  |  |  |  |  | 
Specifications: | 19’ - 2 each, ACS |  |  |  |  |  | 
 | 20’ - 1 each, ACS |  | 4 each, HAK |  |  |  | 
 | 22’ - 11 each, ACS |  | 5 each, CPAI |  |  |  | 
 | 7 each, HAK |  |  |  |  |  | 
 | 28’ - 2 each, ACS |  | 1 each, HAK |  |  |  | 
Function: | Transport personnel, equipment and deploy boom in rivers and near-shore response. |  |  |  |  |  | 
18

## Slide 35
Outboards |  |  |  | 
Quantity: | 49 Total |  |  | 
Manufacturer: | Evinrude, Honda, Johnson, Prodrive, Suzuki and Yamaha |  |  | 
Owner(s): | 24 each, ACS |  | 10 each, CPAI | 1 each, ENI
 | 13 each, HAK |  | 1 each, Savant | 
Specifications: | 9 Jet Units: 25 to 115 HP |  |  | 
 | 40 Prop Units: 4 to 300 HP |  |  | 
Function: | Power non-inboard engine vessels. |  |  | 
19

## Slide 36
This page intentionally left blank.

## Slide 37
Recovery Equipment
Section C

## Slide 38
This page intentionally left blank.

## Slide 39
LORI Brush Skimmers |  |  | 
Quantity: | 12 Total |  | 
Manufacturer: | LORI |  | 
Owner(s): | 10 each, ACS | 2 each, HAK | 
Specifications: | 8 each, LSC-3 4 each, LFS-3 (without brushes) |  | 
 | Nameplate Capacity: 271 BPH Derated Capacity: 217 BPH |  | 
Function: | Advancing brush skimmer for the recovery of heavy oils in open ocean conditions. LORI Side Collector (LSC) - Vessel based oleophilic chain brush skimmer designed for advancing skimming operations in the near shore and open ocean environment. Skimmer is capable of recovery speeds up to 3 knots and adaptable to varying oil viscosities via interchangeable brush cassettes. Integral positive displacement Desmi 250 transfer pump capable of pumping highly viscous fluids. LORI Floating Skimmer (LFS) - Independent oleophilic chain brush skimmer designed for advancing skimming operations in the near shore and open ocean environment. Skimmer can effectively be towed, pushed or affixed to the side of a vessel. Skimmer is capable of recovery speeds up to 3 knots and adaptable to varying oil viscosities via interchangeable brush cassettes. Integral positive displacement Desmi 250 transfer pump capable of pumping highly viscous fluids. |  | 
Auxiliary Equip: | Hydraulic power pack and vessel for advancing skimmer |  | 
20

## Slide 40
Vikoma Weir Skimmers |  | 
Quantity: | 5 Total | 
Manufacturer: | Vikoma | 
Owner(s): | ACS | 
Specifications: | 4 each, Mini Fasflow 1 each, Fasflow | Nameplate Capacity: 143 BPH Derated Capacity: 29 BPH Nameplate Capacity: 486 BPH Derated Capacity: 97 BPH
Function: | Spill recovery in fast moving water. | 
Auxiliary Equip: | 3” Diaphragm Pump with Mini or 3” Sykes Univac with Fasflow | 
21

## Slide 41
Foxtail Rope Mop Skimmer |  |  | 
Foxtail 1-6 |  |  | Foxtail 4-9
Quantity: | 3 Total |  | 
Manufacturer: | Hendriksen |  | 
Owner(s): | ACS |  | 
Specifications: | 2 each, Foxtail 1-6 | Nameplate Capacity: 19 BPH Derated Capacity: 15 BPH | 
 | 1 each, Foxtail 4-9 | Nameplate Capacity: 249 BPH Derated Capacity: 119 BPH | 
Function: | Near-shore and shore recovery responses. Very good skimmer for broken ice conditions. |  | 
Auxiliary Equip: | Hydraulic power pack, recovery tank |  | 
22

## Slide 42
Desmi Skimmers (Harbor and Ocean) |  |  | 
Quantity: | 3 Total |  | 
Manufacturer: | Desmi |  | 
Owner(s): | 2 each, ACS | 1 each, CPAI | 
Specifications: | 2 each, Habor*: | Nameplate Capacity: 440 BPH Derated Capacity: BPH | 
 | *When changed over to brush : 3 each | Nameplate Capacity changes to: 171 BPH Derated Capacity: 137 BPH 1 with brush kit | 
 | 1 each, Ocean: | Nameplate Capacity: 628 BPH Derated Capacity: 91BPH | 
Function: | The Desmi Skimmer is of weir type. Rated for recovery from offshore and near-shore environments. |  | 
Auxiliary Equip: | Hydraulic hoses, discharge hoses, power pack or Quattro brush adapter |  | 
23

## Slide 43
Disc Skimmers |  |  | 
Vikoma Komara Morris Vikoma Komora Star |  |  | 
Quantity: | 25 Total |  | 
Manufacturer: | Morris International Trading Ltd. and Vikoma (12k and 30k) |  | 
Owner(s): | 5 each, ACS | 3 each, CPAI | 
 | 17 each, HAK |  | 
Specifications: | 1 each, Komara Star Heavy Oil Skimmer | Nameplate Capacity: 20 BPH Derated Capacity: 16 BPH | 
 | 3 each, MI-11/24: | Nameplate Capacity: 29 BPH Derated Capacity: 3 BPH | 
 | 8 each, Komara 12K: | Nameplate Capacity: 100 BPH Derated Capacity: 10 BPH | 
 | 3 each, MI-30: | Nameplate Capacity: 143 BPH Derated Capacity: 10 BPH | 
 | 10 each, Komara 30K: | Nameplate Capacity: 189 BPH Derated Capacity: 10 BPH | 
Function: | Near-shore and on-shore use. This skimmer contains three sets of oleophilic (oil attracting) discs. The discs rotate down through the oil layer where free floating oil attaches to the surface of the discs. Inside the skimmer, scrapers remove the oil, which is then pumped to storage containers. |  | 
Auxiliary Equip: | Power packs and hoses |  | 
24

## Slide 44
Drum/Brush Skimmers |  |  |  |  | 
Aqua Guard |  |  | Elastec Groovy Drum |  | 
Lamor |  |  | Action Petroleum |  | 
Quantity: | 36 Total |  |  |  | 
Manufacturer: | Action Petroleum, Aqua Guard, Elastec American Marine, Komara, and Lamor |  |  |  | 
Owner(s): | 11 each, ACS | 20 each, CPAI |  |  | 
 | 2 each, ENI | 3 each, HAK |  |  | 
Specifications: | Drums range from 6.5” to 36” Nameplate Capacity: 33 to 314 BPH Derated Capacity: 26 to 110 BPH |  |  |  | 
Function: | Recovery of refined fuels and crude oil from near-shore and inland waters. |  |  |  | 
Auxiliary Equip: | Hydraulic or air power sources |  |  |  | 
25

## Slide 45
Grooved Drum Skimmer w/Steam Coils and Steam Trailers |  |  | 
Quantity: | 10 skimmers, 2 steam trailers |  | 
Manufacturer: | Elastec American Marine |  | 
Owner(s): | 3 each, skimmer, ACS |  | 1 each, skimmer, CPAI
 | 6 each, skimmer, HAK |  | 
 | 1 each, trailer, ACS |  | 1 each, trailer HAK
Specifications: | TDS-118 Grooved Nameplate Capacity: 33 BPH Derated Capacity: 7 BPH |  | 
 | Magnum 100, 4-Drum skimmer Nameplate Capacity: 228 BPH Derated Capacity: 46 BPH |  | 
Function: | Recovery of refined fuels and crude oil near-shore and inland |  | 
 | waters, particularly during freeze up conditions. |  | 
Auxiliary Equip: | Hydraulic power source and independent pump unit. |  | 
26

## Slide 46: Crucial Fuzzy Disc Skimmer
Quantity: | 10 Total |  |  | 
Manufacturer: | Crucial |  |  | 
Owner(s): | 9 each, ACS | 1 each, HAK |  | 
Specifications: | 4 each, Model 13/24 Nameplate Capacity: 121 BPH Derated Capacity: 24 BPH 6 each, Model 13/30 Nameplate Capacity: 200 BPH Derated Capacity: 40 BPH |  |  | 
Function: | Oil recovery from on water operations. |  |  | 
Auxiliary Equip: | Hydraulic power unit and pump |  |  | 
27

## Slide 47: Crucial Fuzzy Drum Skimmer
Quantity: | 6 Total |  |  | 
Manufacturer: | Crucial |  |  | 
Owner(s): | 4 each, ACS | 1 each, ENI |  | 1 each, HAK
Specifications: | Model #1CD18H-36 Nameplate Capacity: 120 BPH Derated Capacity: 24 BPH |  |  | 
Function: | Oil recovery from on water operations. |  |  | 
Auxiliary Equip: | Hydraulic power unit, 3” pump |  |  | 
28

## Slide 48
Lamor Brush Belt Skimmers and Rock Cleaners |  | 
 |  | Rock Cleaner Attachment
Quantity: | 13 Total | 
Manufacturer: | Lamor | 
Owner(s): | 1 each, MM-30, CPAI 8 each, MM-20, CPAI | 
 | 2 each, Rock Cleaners, CPAI 2 each, LAM 12, ACS | 
Specifications: | Nameplate Capacity: 75 to 252 BPH Derated Capacity: 60 to 201 BPH | 
Function: | Recover diesel or crude product from the water or rock surfaces. | 
Auxiliary Equip: | Hydraulic or air power sources | 
29

## Slide 49
Skimmer Rope Mops |  |  |  |  | 
Quantity: | 32 Total |  |  |  | 
Manufacturer: | Centrifugal Systems, Containment Systems Corporation, Crucial, and Oil Mop |  |  |  | 
Owner(s): | 14 each, ACS | 9 each, CPAI |  |  | 
 | 8 each, HAK | 1 each, Savant |  |  | 
Specifications: | Electric and diesel powered 4” Rope Mops |  |  | Nameplate Capacity: 14 BPH Derated Capacity: 5 BPH | 
Function: | Recover hydrocarbons from shallow water, broken ice and tundra in polygonal trenches. |  |  |  | 
Auxiliary Equip: | Two 4” x100’ mops, two return pulleys and one containment drum with pallet |  |  |  | 
30

## Slide 50
SeaVac Heli-Skimmer |  | 
Quantity: | 1 Total | 
Manufacturer: | Kepner Products | 
Owner(s): | ACS | 
Specifications: | Nameplate Capacity: 944 BPH Derated Capacity: 189 BPH | 
Function: | Advancing weir skimmer for the recovery of heavy or emulsified oils in protected waters. | 
Auxiliary Equip: | Outboard motor, and 2”-3” trash pumps | 
31

## Slide 51
Manta Ray Skimmers |  |  | 
Quantity: | 47 Total |  | 
Manufacturer: | Slickbar |  | 
Owner(s): | 3 each, ACS | 16 each, CPAI | 
 | 28 each, HAK |  | 
Specifications: | Nameplate Capacity: 54 BPH Derated Capacity: 11 BPH |  | 
 | 10 Flexible 37 Rigid |  | 
Function: | Recovery of thin oil layers and sheen in protected waters. |  | 
Auxiliary Equip: | 3” Diaphragm pump or Peristaltic pump |  | 
32

## Slide 52
Vac Units |  |  |  | 
Quantity: | 7 Total |  |  | 
Manufacturer: | Vikoma, Vac-U-Max |  |  | 
Owner(s): | HAK |  |  | 
Specifications: | Vac-U-Max: |  | TK-01, TK-02, TK-1-B, 23956 | 
 | Vikoma: |  | Power Vac | 
Function: | Air and diesel driven vacuum units for spill recovery inside fixed structures or flat hard surfaces. |  |  | 
Auxiliary Equip: | Air compressor or auxiliary power unit |  |  | 
33

## Slide 53
Mini Vac Units & Tanks |  |  |  | 
Quantity: | 5 Total Mini Vac Units, 2 Total Tanks |  |  | 
Manufacturer: | Elastec American Marine |  |  | 
Owner(s): | 2 each, ACS |  | 1 each, CPAI | 
 | 2 each, HAK |  |  | 
 | 1 each, tank, CPAI |  | 1 each, tank, HAK | 
Specifications: | 20 HP power unit |  |  | 
Function: | Recovery of product in remote, or “off site” locations. |  |  | 
Auxiliary Equip: | 55 gallon open top drums, 110 gallon all-terrain tracked tank, ATV or snow machine for transport |  |  | 
34

## Slide 54
Air Power Units |  | 
Quantity: | 3 Total | 
Manufacturer: | Elastec American Marine | 
Owner(s): | 1 each, ACS | 2 each, CPAI
Specifications: | Diesel powered | 
Function: | Power unit designed to operate air drum skimmers as an all in one unit. Power unit equipped with air compressor and peristaltic pump. | 
35

## Slide 55
Snow Blowers |  |  | 
Quantity: | 6 Total |  | 
Manufacturer: | Honda |  | 
Owner(s): | 2 each, ACS | 2 each, CPAI | 
 | 1 each, ENI | 1 each HAK | 
Specifications: | Gas operated with the ability to move up to 35 tons/hr of snow. 2.5 hours of operating time per fuel tank |  | 
Function: | Remove contamination from the snow surface. |  | 
36

## Slide 56
Gas and Propane Powered Ice Augers |  |  | 
Quantity: | 39 Total |  | 
Manufacturer: | Ardisam, Feldman Engineering, General Equipment Co., and Strike Master |  | 
Owner(s): | 7 each, ACS | 12 each, CPAI | 3 each, ENI
 | 16 each, HAK | 1 each, Savant | 
Specifications: | One and two person units 34 CC to 102 CC |  | 
Function: | Drill through ice to the water interface. This technique is used for product detection and recovery. |  | 
Auxiliary Equip: | Bits and extensions |  | 
37

## Slide 57
Jackhammers |  |  | 
Quantity: | 20 Total |  | 
Manufacturer: | DeWalt and Ingersoll Rand |  | 
Owner(s): | 6 each, ACS | 3 each, CPAI | 5 each, ENI
 | 5 each, HAK | 1 each, Savant | 
Specifications: | One and two person units 13 each, air powered 7 each, electric |  | 
Function: | Break up contaminated ice or ground for recovery. |  | 
Auxiliary Equip: | Compressor or generator, hose, whip check, paddles/bits, tanner gas. |  | 
38

## Slide 58
Chainsaws and Ice Trenching Tools |  |  |  |  |  | 
Quantity: | 49 Total (chainsaws) |  |  |  |  | 
Manufacturer: | Homelite-Textron and Stihl |  |  |  |  | 
Owner(s): | 11 each, ACS |  | 13 each, CPAI |  |  | 
 | 4 each, ENI |  | 21 each, HAK |  |  | 
Specifications: | 18” to 48” chainsaw bar |  |  |  |  | 
Function: | Trench and remove ice for winter containment and recovery. |  |  |  |  | 
Note: | Various chipping bars and ice tongs are stocked at each location |  |  |  |  | 
39

## Slide 59
Rube Witches |  |  |  | 
Quantity: | 9 Total |  |  | 
Manufacturer: | ACS |  |  | 
Owner(s): | 7 each, ACS |  | 2 each, CPAI | 
Specifications: | 36” chainsaw bar required |  |  | 
Function: | Cut trenches in the ice or to cut out blocks of ice to be used in recovery techniques. Provides a safe platform for chainsaw use. |  |  | 
Auxiliary Equip: | Stihl 056 or 066 chain saw with ice cutting chain |  |  | 
40

## Slide 60
This page intentionally left blank.

## Slide 61
Containment
Section D

## Slide 62
This page intentionally left blank.

## Slide 63
Delta/River Boom |  |  | 
Quantity: | 203,776 ft. |  | 
Manufacturer: | Abasco, American Boom, American Marine, Containment Systems Inc., D.U. Inc., Elastec, Elastec American Marine, Lamor, SG&J Loxley AL, Texas Boom Company, and USA MFG |  | 
Owner(s): | 60,500 ft., ACS | 55,926 ft., CPAI | 
 | 79,700 ft., HAK | 7,650 ft., Savant | 
Specifications: | 10”, 14” and 16” x 50’ and 75’ Sections Delta Boom- Bottom Tension only - 28,850 ft. River Boom- Top and Bottom Tension- 174,926 ft. |  | 
Function: | Containment and control of oil in a river environment. Pre-staged at remote river sites in connexs for airboat deployment. |  | 
Auxiliary Equip: | Connexs, anchors and airboats |  | 
41

## Slide 64
Boom Rudders |  |  | 
Quantity: | 90 Total |  | 
Manufacturer: | Envirotech |  | 
Owner(s): | ACS |  | 
Specifications: | 8” diameter x 80” pipe with 12” x 60” deflector wing |  | 
Function: | River booming without the use of midpoint anchor systems. |  | 
Auxiliary Equip: | River boom |  | 
42

## Slide 65
Boom Handler |  |  | 
Quantity: | 1 Total |  | 
Manufacturer: | Seacor Environmental Products |  | 
Owner(s): | ACS |  | 
Specifications: | 60” Roller |  | 
Function: | Recovery of oil spill containment boom. |  | 
43

## Slide 66
Shore Seal Boom |  |  | 
Quantity: | 21,650 ft., Total |  | 
Manufacturer: | Texas Boom and Versa Tech |  | 
Owner(s): | 16,900 ft., ACS | 1,750 ft., CPAI | 
 | 1,000 ft., HAK | 2,000 ft., ENI | 
Specifications: | 20” x 50’ sections |  | 
Function: | Shoreline protection or used as barriers for on land flushing operations. |  | 
Auxiliary Equip: | Air inflator and water pump |  | 
44

## Slide 67
T- Fence Boom |  |  | 
Quantity: | 492 ft., Total |  | 
Manufacturer: | Harbo Technologies |  | 
Owner(s): | ACS |  | 
Specifications: | 2.25’ x 82.021’ sections |  | 
Function: | Light weight one time use boom for Shoreline protection. |  | 
Auxiliary Equip: | Anchors and airboats |  | 
45

## Slide 68
Kepner Boom Reel Packs |  |  |  |  | 
Quantity: | 33,500 ft., Total |  |  |  | 
 | 20” – 4,750 ft. | 26” – 25,750 ft. | 32” – 2,000 ft. |  | 42” – 1,000 ft.
Manufacturer: | Kepner |  |  |  | 
Owners: | 23,250 ft., ACS 1,750 ft., (26”), CPAI |  |  |  | 
 | 5,000 ft., (20”), ENI 3,500 ft., (26”) HAK |  |  |  | 
Specifications: | 20” to 42” x 250’ to 1,500’ per reel |  |  |  | 
Function: | Rapid deployment of boom from shore or support vessel. |  |  |  | 
Auxiliary Equip: | Hydraulic power pack and hoses |  |  |  | 
46

## Slide 69
NOFI Ocean Boom |  |  |  |  |  | 
Quantity: | 5,904 ft. Total |  |  |  |  | 
Manufacturer: | Allmaritim |  |  |  |  | 
Owner(s): | 2,952 ft., ACS |  | 984 ft., ENI |  | 1,968 ft., HAK | 
Specifications: | 5 each, Model 250 – 24”, 984 ft. sections 2 each, Model 350 – 34”, 492 ft. sections |  |  |  |  | 
Function: | Designed for easy transportation and rapid deployment. |  |  |  |  | 
47

## Slide 70
NOFI Harbor Buster |  |  |  |  |  |  |  | 
Quantity: | 2 Total |  |  |  |  |  |  | 
Manufacturer: | NOFI |  |  |  |  |  |  | 
Owner(s): | HAK |  |  |  |  |  |  | 
Size: | 89 ft. long x 50 ft. wide at the mouth |  |  |  |  |  |  | 
Tow Speed: | 3 kts |  |  |  |  |  |  | 
Max Volume: | Total: 3,963 gallons |  |  | In Separator: 1,321 gallons |  |  |  | 
Function: | Designed for recovery of oil at high speeds in open water. Rear pocket separates oil from water and provides a calm recovery point for a skimmer. This can also be used in rivers of sufficient depth that do not exceed 3 kts. |  |  |  |  |  |  | 
Auxiliary Equip: | Boom reel pack, power pack, blower, Boom Vane, tow vessel(s) |  |  |  |  |  |  | 
48

## Slide 71
Ro-Boom |  |  |  |  | 
Quantity: | 2,360 ft., Total |  |  |  | 
Manufacturer: | Ro-Clean Desmi |  |  |  | 
Owner(s): | HAK |  |  |  | 
Specifications: | 59” |  |  |  | 
Function: | Containment of product in waters deeper than 6 ft. |  |  |  | 
Auxiliary Equip: | Hydraulic power pack and hoses |  |  |  | 
49

## Slide 72
Goodyear Ocean Boom |  |  |  | 
Quantity: | 14,300 ft., Total |  |  | 
Manufacturer: | Engineered Fabrics Corporation |  |  | 
Owner(s): | ACS |  |  | 
Specifications: | 42” inflatable |  |  | 
Function: | Containment of product in waters deeper than 6 ft. |  |  | 
Auxiliary Equip: | Power pack, blower and hydraulic hoses |  |  | 
50

## Slide 73
Abasco Harbor Boom |  |  |  | 
Quantity: | 2,000 ft., Total |  |  | 
Manufacturer: | Abasco |  |  | 
Owner(s): | CPAI |  | . | 
Specifications: | 30” Self–inflating, high tensile strength, unsinkable |  |  | 
Function: | Containment of product in a near-shore and offshore environment. |  |  | 
51

## Slide 74
Lamor Boom Reel Packs |  | 
Quantity: | 2 Total | 
Manufacturer: | Lamor Corporation | 
Owner(s): | ACS | 
Specifications: | 50” x 1500’ per reel | 
Function: | Rapid deployment and storage of Lamor boom. | 
Auxiliary Equip: | Self contained with power pack and blower on reel. Power pack also set up to run DOP pumps. | 
52

## Slide 75
Boom Inflating Blowers |  |  | 
Quantity: | 51 Total |  | 
Manufacturer: | Echo, Husqvarna and Stihl |  | 
Owner(s): | 36 each, ACS 4 each, ENI | 5 each, CPAI 6 each, HAK | 
Specifications: | 388 CFM 180 Air Speed at Pipe |  | 
Function: | Boom inflation. |  | 
53

## Slide 76
Floating Pumps 1 1/2” |  |  |  | 
Quantity: | 51 Total |  |  | 
Manufacturer: | Waterous and Hale |  |  | 
Owner(s): | 36 each, ACS | 4 each, CPAI |  | 
 | 2 each, ENI | 6 each, HAK |  | 
Specifications: | 140 GPM @ 30 psi: 200 BPH @ 30 psi |  |  | 
Function: | Fill shoreseal boom with water. |  |  | 
Auxiliary Equip: | Discharge hose |  |  | 
54

## Slide 77
Pipe/Culvert Plugs |  | 
Quantity: | 19 Total | 
Manufacturer: | Cherne and Aero Tech Labs | 
Owner(s): | 6 each, ACS | 13 each, HAK
Specifications: | 1 – 6”, 1 – 8”, 2 – 12 to18”, 7 - 12 to 24”, 2 - 15 to 30”, 6 - 40” | 
Function: | Block pipes or culverts to provide containment during a response. | 
Auxiliary Equip: | Air compressor and hose | 
55

## Slide 78
Water Spray Trailer | 
Quantity: | 1 Total
Manufacturer: | Magnum Fire Systems
Owner(s): | ACS
Specifications: | 12’ trailer with insulated and heated housed fire pump water spray
 | system. Powered by a 4 cylinder air cooled Deutz diesel engine
 | and consists of a 300 gallon fresh water tank.
Function: | Contain misted oil over a snow covered surface for mechanical
 | recovery, particularly when high winds are expected to prevent
 | the misted snow from blowing away.
56

## Slide 79
In-Situ Burn Equipment
Section E

## Slide 80
This page intentionally left blank.

## Slide 81
Helitorch Gelled Fuel Mixers |  | 
Quantity: | 2 Total | 
Manufacturer: | Simplex | 
Owner(s): | ACS | 
Specifications: | 300 gallons, 1 each trailer mounted and 1 each skid mounted | 
Function: | Mix gelled fuel for aerial helitorches. Not DOT approved, must be filled onsite | 
57

## Slide 82
Handheld Igniters | 
Quantity: | Approximately 1,000 units
Manufacturer: | Elastec and Energetex
Owner(s): | ACS
Specifications: | Tin can style with hand held igniter Plastic container filled with gelling agent with float
Function: | Hand held igniter for in-situ burning.
Auxiliary Equip: | Battery pack or an ignition source, handheld flare, fuel
58

## Slide 83
Fire Boom |  |  |  | 
Quantity: | 19,900 ft., Total, (500’ of this is training boom) |  |  | 
Manufacturer: | 3M, Applied Fabrics, and Elastec American Marine |  |  | 
Owner(s): | 16,100 ft., ACS |  | 1,000 ft., CPAI | 
 | 2,800 ft., HAK |  |  | 
Specifications: | Sizes ranging from 20” to 42” 3 M – 10,400 ft. - 20” to 42” Elastec - 6500 ft. - 27” to 33” Hydro Boom Applied - 3000 ft. - 30” Pyro Boom |  |  | 
Function: | Containment of product for in-situ burning. |  |  | 
Auxiliary Equip: | Tow bridles and boat for deployment and means of towing 500’ of Elastec training boom, not suitable for response. |  |  | 
59

## Slide 84
Helitorches |  |  |  | 
Quantity: | 6 Total |  |  | 
Manufacturer: | Simplex |  |  | 
Owner(s): | ACS |  |  | 
Specifications: | 55 gallon |  |  | 
Function: | Ignition of hydrocarbon products during in-situ burn operations. |  |  | 
Auxiliary Equip: | Helicopter remote control box, spare 55 gallon drums |  |  | 
60

## Slide 85
Transfer and Storage
Section F

## Slide 86
This page intentionally left blank.

## Slide 87
Barges 125 BBL |  | 
Quantity: | 2 Total | 
Manufacturer: | North Wind Marine | 
Owner(s): | ACS | 
Specifications: | Draft: 1’ empty, 3’ full 125 bbls, 29’ x 10’x 5’ 5,200 lbs. | 
Function: | Storage and transportation of product from skimming vessels to off loading point. | 
Auxiliary Equip: | Off loading pumps | 
61

## Slide 88
Barges 249 BBL |  | 
Quantity: | 13 Total | 
Manufacturer: | Kvichak Marine Industries | 
Owner(s): | 10 each, ACS | 3 each, HAK
Specifications: | Draft: 1’ empty, 4’ full 249 bbls, 40’ x 11’ x 5’6” 10,875 lbs. | 
Function: | Storage and transportation of product from skimming vessels to off loading point. | 
Auxiliary Equip: | Off loading pumps | 
62

## Slide 89
Barge 650 BBL |  | 
Quantity: | 1 Total | 
Manufacturer: | American Eagle | 
Owner(s): | ACS | 
Specifications: | Draft: 1’ empty, 5’ 6” full 650 bbls, 62’ x 16 ’ x 6’6” 35,000 lbs. | 
Function: | Storage and transportation of product from skimming vessels to off loading point. | 
Auxiliary Equip: | Off loading pumps and hydraulic power unit | 
63

## Slide 90
Viscous Oil Annular Injection Kits |  | 
Quantity: | 4 Total | 
Manufacturer: | Hyde and Ro-Clean Desmi | 
Owner(s)/Location: | ACS | 
Specifications: | 1 each, 3” annular injection rings 1 each, 4” annular injection rings 2 each, 6” annular injection rings | 
Function: | Enhance viscous oil pumping capabilities. | 
Auxiliary Equip: | Discharge hose, hydraulic power pack and water injection pump, cargo pump | 
64

## Slide 91
Fastank/Fold-A-Tanks |  |  |  |  | 
Quantity: |  |  | 170 Total |  | 
Manufacturer: |  |  | Areo Tech, The Eldred Environmental, Fast Engineering, Fold-A-Tank, and Vikoma |  | 
Owner(s): |  |  | 34 each, ACS | 78 each, CPAI | 6 each, ENI
 |  |  | 46 each, HAK | 6 each, Savant | 
Specifications: |  |  | Fastank/Fold-A-Tanks/Open Top Tank 400 to 3,000 gallons |  | 
Function: |  |  | Temporary storage of recovered product. |  | 
65

## Slide 92
Self Rising Tanks |  | 
Quantity: | 48 Total | 
Manufacturer: | Canflex | 
Owner(s): | 10 each, ACS | 38 each, CPAI
Specifications: | Self rising, 2,500 gallons | 
Function: | Temporary storage of recovered product. | 
66

## Slide 93
Floating Tank |  | 
Quantity: | 1 Total | 
Manufacturer: | Qualitech Environmental | 
Owner(s): | CPAI | 
Specifications: | 2100 gallons | 
Function: | This tank can be placed under a leaking pipeline that is over a body of water. The tank is secured in place with anchors. This can also be used on tundra. | 
67

## Slide 94
Upright Tank |  | 
Quantity: | 1 Total | 
Manufacturer: | ConocoPhillips | 
Owner(s): | CPAI | 
Specifications: | 16,800 gallons: 400 bbls, plus approximately 150 additional tanks available on the Slope ranging in size from 40 to 500 bbls. | 
Function: | Storage of recovered product and flushing operations. | 
68

## Slide 95
Bladders |  |  | 
Quantity: | 24 Total |  | 
Manufacturer: | Canflex and Areo Tech Labs |  | 
Owner(s): | 2 each, 500 gal., ACS |  | 3 each, 500 gal., CPAI
 | 8 each, 1,320 gal., ACS |  | 6 each, 2,640 gal., ACS
 | 5 each, 5,000 gal., CPAI |  | 
Specifications: | 500 to 5,000 gallons, Towable, Pillow, Tow/Lift |  | 
Function: | Store and transport recovered product. |  | 
Auxiliary Equip: | Boat, helicopter |  | 
69

## Slide 96
Heavy Oil Pumps |  | 
Quantity: | 21 Total | 
Manufacturer: | Desmi, Lamor and Elastec American Marine | 
Owner(s): | 18 each, ACS | 2 each, HAK
 | 1 each, CPAI | 
Specifications: | 3”- 2 each, 110 GPM, 157 BPH 3”- 2 each, 132 GPM, 188 BPH 6”- 17 each, 440 GPM, 628 BPH | 
Function: | Transferring heavy oils. | 
Auxiliary Equip: | Hydraulic power pack, double hose reel with discharge and hydraulic hoses. Light oil adapter and water injection kits. | 
70

## Slide 97
Air Diaphragm Pumps ½”, 1”, 2” and 3” |  |  |  | 
Quantity: | 20 Total |  |  | 
Manufacturer: | Ingersoll-Rand and Wilden |  |  | 
Owner(s): | 6 each (1/2”), HAK |  | 6 each (1”), HAK | 
 | 6 each (2”), HAK |  | 1 each (2”), ENI | 
 | 1 each (3”), CPAI |  |  | 
Specifications: | 15 to 260 GPM, 21 to 371 BPH |  |  | 
Function: | Transfer of product from a recovery point to a set storage area. |  |  | 
Auxiliary Equip: | Air compressor, air hose and suction/discharge hose |  |  | 
71

## Slide 98
Diesel/Hydraulic Diaphragm Pumps 2” and 3” |  |  |  | 
Quantity: | 50 Total |  |  | 
Manufacturer: | Aqua Guard, Gormann Rupp, and Yanmar |  |  | 
Owner(s): | 32 each, ACS | 7 each, CPAI |  | 
 | 3 each, ENI | 8 each, HAK |  | 
Specifications: | 3 each, 2” diesel pumps |  | 1 each, 2” hydraulic pump | 
 | 40 each, 3” diesel pumps 6 each, 3” hydraulic pumps 86-100 GPM, 123-142 BPH |  |  | 
Function: | Transfer of product from a recovery point to a set storage area. |  |  | 
Auxiliary Equip: | Suction and discharge hose |  |  | 
72

## Slide 99
Gas Diaphragm Pumps 3” |  |  |  | 
Quantity: | 12 Total |  |  | 
Manufacturer: | Homelite-Textron and Honda |  |  | 
Owner(s): | 9 each, CPAI | 3 each, HAK |  | 
Specifications: | 80 GPM, 114 BPH |  |  | 
Function: | Transfer of product from a recovery point to a set storage area. |  |  | 
Auxiliary Equip: | Suction and discharge hose |  |  | 
73

## Slide 100
Diesel/Hydraulic Peristaltic Pumps 2”, 2 ½”, and 3” |  |  |  |  | 
Quantity: | 19 Total |  |  |  | 
Manufacturer: | Diesel America West and Salaroll |  |  |  | 
Owner(s): | 7 each, ACS | 6 each, CPAI |  |  | 
 | 2 each, ENI | 4 each, HAK |  |  | 
Specifications: | 53-115 GPM, 75-164 BPH |  |  |  | 
Function: | Transfer of product from a recovery point to a set storage area. |  |  |  | 
Auxiliary Equip: | Suction and discharge hose |  |  |  | 
74

## Slide 101
Sykes Univac Diesel Pump 3” |  | 
Quantity: | 1 Total | 
Manufacturer: | Sykes | 
Owner(s): | ACS | 
Specifications: | 340 GPM, 485 BPH | 
Function: | Transfer of product from a recovery point to a set storage area. | 
Auxiliary Equip: | Suction and discharge hose | 
75

## Slide 102
Centrifugal Pumps 2”, 3” and 4” |  |  |  |  |  | 
Quantity: | 115 Total |  |  |  |  | 
Manufacturer: | Diesel America West, Elastec American Marine, Gorman-Rupp, Honda, Multi-Quip, and Yanmar |  |  |  |  | 
Owner(s): | 52 each, ACS | 28 each, CPAI |  |  |  | 
 | 2 each, ENI | 31 each, HAK |  |  |  | 
 | 2 each, Savant |  |  |  |  | 
Specifications: | 2 each, 1”, 32 GPM, 46 BPH Gas 2 each, 1 ½”, 74 GPM, 106 BPH Gas 30 each, 2” up to 220 GPM, 314 BPH 56 each, 3” up to 400 GPM, 571 BPH 17 each, 4” 370-750 GPM, 528-1,071 BPH |  |  |  |  | 
 | 8 each, 4” Fire Boom Pumps, Elastec American Marine |  |  |  |  | 
Function: | Transfer of product from a recovery point to a set storage area. |  |  |  |  | 
Auxiliary Equip: | Suction and discharge hose |  |  |  |  | 
76

## Slide 103
Emergency Dewatering Pumps 2” |  |  | 
Quantity: | 6 Total |  | 
Manufacturer: | Ohler Machinery |  | 
Owner(s): | ACS |  | 
Specifications: | 230 GPM, 329 BPH |  | 
Function: | Emergency dewatering pump for vessels in distress. |  | 
Auxiliary Equip: | Suction and discharge hose |  | 
77

## Slide 104
This page intentionally left blank.

## Slide 105
Logistics Support Equipment
Section G

## Slide 106
This page intentionally left blank.

## Slide 107
Centaur 950DT |  | 
Quantity: | 3 Total | 
Manufacturer: | Ontario Drive & Gear Limited | 
Owner(s): | 2 each, CPAI 1 each, HAK | 
Specifications: | Diesel powered amphibious tracked vehicle. | 
Function: | All-season cross-country transportation of equipment and personnel. | 
Auxiliary Equip: | Trailer, electric winch | 
78

## Slide 108
4-Wheelers |  |  |  | 
Quantity: | 11 Total |  |  | 
Manufacturer: | Con-Am and Honda |  |  | 
Owner(s): | 3 each, CPAI | 8 each, HAK |  | 
Specifications: | Gasoline ATV 282cc to 500cc |  |  | 
Function: | Transportation of equipment. |  |  | 
Auxiliary Equip: | Snow plow, trailers on wheels, trailers on skis and an electric winch |  |  | 
79

## Slide 109
Kubotas with Tracks |  |  |  | 
Quantity: | 12 Total |  |  | 
Manufacturer: | Kubota |  |  | 
Owner(s): | 5 each, ACS | 2 each, ENI |  | 
 | 5 each, HAK |  |  | 
Specifications: | 3 cylinder diesel (22 - 25HP) |  |  | 
Function: | Transportation of equipment. |  |  | 
Auxiliary Equip: | Snow plow, electric winch, trailers |  |  | 
80

## Slide 110
Tucker Sno-Cat |  |  |  | 
Quantity: | 1 Total |  |  | 
Manufacturer: | Tucker Terra |  |  | 
Owner(s): | HAK |  |  | 
Specifications: | Model: 1643E-26-6 14 person 100 gallon fuel tank, 14,000 lbs. |  |  | 
Function: | Transportation of personnel and equipment. |  |  | 
Auxiliary Equip: | Snow plow, electric winch, trailers |  |  | 
81

## Slide 111
Bobcat Tool Cat 5600 |  | 
Quantity: | 1 Total | 
Manufacturer: | Bobcat | 
Owner(s): | CPAI | 
Specifications: | 4x4 All Terrain Vehicle with 40 plus attachments | 
Function: | Daily use for spill response/cleanup, moving/lifting equipment, snow removal and transportation around the pad. It can call 2,000 lbs. in cargo box and tow 4,000 lbs. plus lift over 1,500 lbs. to a height of 7 feet. | 
Auxiliary Equip | Hydraulic concrete/ice breaker, two types of snow/ice/gravel scrapers, bucket, forks, pintle hitch, and a sweeper. | 
82

## Slide 112
Snow Machines and Sleds |  | 
Quantity: | 42 Total snow machines and 37 Total sleds | 
Manufacturer: | Snow Machines: SKI-DOO and Polaris Sleds: Alaska Frontier Fabricators, Last Frontier Trailers Plashem, Tag-a-long Trailers, Team Otter Outdoors | 
Owner(s): | 8 each, snow machines, ACS | 14 each, snow machines, CPAI
 | 4 each, snow machines, ENI | 16 each, snow machines, HAK
 | 15 each, sled, ACS | 8 each, sled, CPAI
 | 4 each, sled, ENI | 10 each, sled, HAK
Specifications: | Short and long track 250cc to 660cc | 
Function: | Transportation of equipment and personnel. | 
83

## Slide 113
Muck Truck Motorized Wheelbarrow |  | 
Quantity: | 2 Total | 
Manufacturer: | Muck Truck USA | 
Owner(s): | ACS | 
Specifications: | Model: Max-truck® with Honda GXV 4.3 HP 4-stroke engine. | 
 | Peerless 4 forward 1 reverse transmission | 
 | Speed: 0-3.5 mph | 
 | Capacity of 8 cu/ft. – 800 lbs. carrying capacity | 
 | Dimensions: Length 63” x Width 28” x Height 36” | 
 | Weight: 280 lbs. | 
 | Traction: 4 Wheel drive. | 
Function: | Transport contaminated material from the spill site to the collection area. | 
84

## Slide 114
Passenger/Work Vehicles |  |  |  |  |  | 
Quantity: | 11 Total |  |  |  |  | 
Manufacturer: | Ford Motor Company |  |  |  |  | 
Owner(s): | ACS |  |  |  |  | 
Specifications: | 10 each, gasoline |  |  |  |  | 
 | 1 each, diesel |  |  |  |  | 
Function: | Logistical support for spills and ACS daily activities. |  |  |  |  | 
85

## Slide 115
14 Passenger Bus |  |  |  |  |  | 
Quantity: | 1 Total |  |  |  |  | 
Manufacturer: | Ford Motor Company |  |  |  |  | 
Owner(s): | ACS |  |  |  |  | 
Specifications: | 1 each, gasoline |  |  |  |  | 
Function: | Logistical support for spills and ACS daily activities. |  |  |  |  | 
86

## Slide 116
Medium Duty Flatbed |  |  |  | 
Quantity: | 1 Total |  |  | 
Manufacturer: | Freightliner |  |  | 
Owner(s): | ACS |  |  | 
Specifications: | 2009 Freightliner, 330 HP Diesel, 4 x 4, 22’ flatbed, extended cab |  |  | 
Function: | Logistical support for day-to-day operations and spill response activities. |  |  | 
87

## Slide 117
Truck Tractors |  |  |  | 
Quantity: | 2 Total |  |  | 
Manufacturer: | Autocar and Peterbilt |  |  | 
Owner(s): | 1 each, ACS | 1 each, HAK |  | 
Specifications: | Triple-axle tractor |  |  | 
Function: | Logistical support for day-to-day operations and spill response activities. |  |  | 
Auxiliary Equip: | 40’ flat bed cargo trailer, 50’ step deck equipment trailer |  |  | 
88

## Slide 118
Boom Trucks |  |  |  | 
Quantity: | 2 Total |  |  | 
Manufacturer: | GMC and International |  |  | 
Owner(s): | 1 each, ACS | 1 each, HAK |  | 
Function: | Logistical support for day-to-day operations and spill response activities. |  |  | 
89

## Slide 119
Mechanics’ Trailers |  |  |  |  |  | 
Quantity: | 2 Total |  |  |  |  | 
Manufacturer: | Haulmark and Wells Cargo |  |  |  |  | 
Owner(s): | 1 each, ACS |  | 1 each, CPAI |  |  | 
Function: | Mobile maintenance shop for field support. |  |  |  |  | 
Auxiliary Equip: | 12kw generator / 10kw generator, electric air compressor and various hand tools |  |  |  |  | 
90

## Slide 120
Dump Truck |  |  | 
Quantity: | 1 Total |  | 
Manufacturer: | Autocar |  | 
Owner(s): | HAK |  | 
Function: | Transport contaminated material from spill sites. |  | 
91

## Slide 121
Dempster System Equipped Trucks |  |  |  | 
Quantity: | 1 Total |  |  | 
Manufacturer: | Autocar |  |  | 
Owner(s): | HAK |  |  | 
Specifications: | Dempster hydraulic system |  |  | 
Function: | Transport staging, related equipment and contaminated material to and from spill sites. |  |  | 
Auxiliary Equip: | Dempster equipment system, dump box, connex flat |  |  | 
92

## Slide 122
Skid Steer Loaders |  |  |  | 
Quantity: | 14 Total |  |  | 
Manufacturer: | Bobcat and Caterpillar |  |  | 
Owner(s): | 6 each, ACS | 2 each, CPAI |  | 
 | 1 each, ENI | 5 each, HAK |  | 
Specifications: | 1 each, Model: 299 DXHP |  |  | 
 | 8 each, Model: MT-55 |  |  | 
 | 1 each, Model: T320-G |  |  | 
 | 1 each, Model: T250-G |  |  | 
 | 3 each, Model: 287C |  |  | 
Function: | Performs various functions needed for spill response and field support. |  |  | 
Auxiliary Equip: | Trencher, forks, bucket, auger, sweeper, trimmer, scratcher, jack hammer, snow blower and pintle hitch |  |  | 
93

## Slide 123
Warehouse Fork Lifts |  | 
Quantity: | 3 Total | 
Manufacturer: | Caterpillar, Clark, and Hyster | 
Owner(s): | ACS | 
Specifications: | Caterpillar: 1 each, 6,000 lbs. lifting capacity Clark: 1 each, 9,000 lbs. lifting capacity Hyster: 1 each, 7,000 lbs. lifting capacity | 
Function: | Move and load equipment for day-to-day operations and response activities. | 
Auxiliary Equip: | Pintle hitch attachment and man basket | 
94

## Slide 124
Front End Loaders w/attachments |  |  |  | 
Quantity: | 2 Total |  |  | 
Manufacturer: | Volvo L110H |  |  | 
Owner(s): | ACS |  |  | 
Specifications: | Volvo L110H – 22,280 lbs. lifting capacity |  |  | 
Function: | Move and load equipment for day-to-day operations, response activities and snow removal. |  |  | 
Auxiliary Equip: | Forks, bucket and pintle hitch attachment, snow plow, scratcher |  |  | 
95

## Slide 125
Mobile Command Centers |  |  |  |  |  |  | 
Quantity: | 3 Total |  |  |  |  |  | 
Manufacturer: | Miscellaneous Builders |  |  |  |  |  | 
Owner(s): | 1 each, ACS |  | 1 each, CPAI |  |  |  | 
 | 1 each, HAK |  |  |  |  |  | 
Function: | Provides a center of operations and communications at spill locations. |  |  |  |  |  | 
Auxiliary Equip: | Diesel generator, tractor trailer or truck with dempster system |  |  |  |  |  | 
96

## Slide 126
Staging Area Manager Offices |  |  |  |  | 
Quantity: | 3 Total |  |  |  | 
Manufacturer: | ATCO and Homemade |  |  |  | 
Owner(s): | 1 each, CPAI |  | 2 each, HAK |  | 
Specifications: | 16’ to 40’ |  |  |  | 
Function: | Staging Area Managers’ offices. |  |  |  | 
Auxiliary Equip: | Computer and generator |  |  |  | 
97

## Slide 127
Winter Response Vans |  | 
Quantity: | 1 Total | 
Manufacturer: | Wells Cargo | 
Owner(s): | HAK | 
Specifications: | 20’ | 
Function: | Designed to transport containment and recovery equipment for initial winter response operations. | 
Auxiliary Equip: | Tow vehicle and generator | 
98

## Slide 128
Tanker Rollover Van |  | 
Quantity: | 1 Total | 
Manufacturer: | Wells Cargo | 
Owner(s): | HAK | 
Specifications: | 20’ | 
Function: | All in one rapid response trailer for source control and recovery of product in a rolled over tanker. | 
Auxiliary Equip: | Tow vehicle | 
99

## Slide 129
Steam Van |  | 
Quantity: | 1 Total | 
Manufacturer: | Spill Buster | 
Owner(s): | CPAI | 
Specifications: | 24’ | 
Function: | All in one response van that contains equipment to conduct high pressure hot water cleaning | 
Auxiliary Equip: | Dempster system equipped truck | 
100

## Slide 130
Warm Up/Break Shacks |  |  |  | 
Quantity: | 5 Total |  |  | 
Manufacturer: | Arctic Structures, Atco, Britco, and Homemade |  |  | 
Owner(s): | 2 each, ACS | 1 each, CPAI |  | 
 | 2 each, HAK |  |  | 
Specifications: | 20’ to 40’ |  |  | 
Function: | Provide area for responders to warm up and take breaks. |  |  | 
Auxiliary Equip: | Generator |  |  | 
101

## Slide 131
Portable Shelters |  |  |  |  | 
Quantity: | 53 Total |  |  |  | 
Manufacturer: | Air-Lite, Eureka, Hanson, and Zumro |  |  |  | 
Owner(s): | 24 each, ACS |  | 11 each, CPAI |  | 2 each, ENI
 | 15 each, HAK |  | 1 each, Savant |  | 
Specifications: | Sizes vary from 7’ x 8’, 12’ x 10’, 12’ x 15’, 13.5’ x 16’ and 12’ x 20’, 26’ x 64’, 12’ x 12’, 13.5’ x 21’ |  |  |  | 
Function: | Protection from environmental conditions for equipment and personnel. |  |  |  | 
Auxiliary Equip: | Flooring and stoves are available for some styles, Zodi tent heater |  |  |  | 
102

## Slide 132
Portable Shops |  |  |  |  | 
Quantity: | 2 Total |  |  |  | 
Manufacturer: | Griffard Steel Inc. and Homemade |  |  |  | 
Owner(s): | ACS |  |  |  | 
Specifications: | 10’ w x 21’ l x 11.5’ h door 103” wide x 96” high 15,000 lbs. 14’W x 48.5’L 15.5’H Door 30,000 lbs. |  |  |  | 
Function: | Protection from environmental conditions for equipment maintenance and repair. |  |  |  | 
Auxiliary Equip: | Generator, heater |  |  |  | 
103

## Slide 133
Portable Restroom Units |  |  | 
Quantity: | 15 Total |  | 
Manufacturer: | Ameri-can Engineering, Britco, Envirovac, Polyjohn, and Sealand |  | 
Owner(s): | 2 each, Envirovac , ACS |  | 1 each, Envirovac, CPAI
 | 2 each, Envirovac, HAK |  | 
 | 4 each, Portable toilets, ACS |  | 4 each, Portable toilets, CPAI
 | 2 each, Portable toilets, HAK |  | 
Specifications: | 24’ to 33’ long, male/female capable |  | 
Function: | Provide on-site restroom facilities during response operations. |  | 
Auxiliary Equip: | Generator |  | 
104

## Slide 134
Indirect Fired Heaters |  | 
Quantity: | 10 Total | 
Manufacturer: | Arcotherm, Equipment Source, Industrial Commercial, Jetheat, Tioga, and Zodi Outback Gear | 
Owner(s): | 7 each, ACS | 3 each, CPAI
Specifications: | 2 each, 70,000 BTU 1 each, 380,000 BTU 2 each, 420,000 BTU 1 each, 500,000 BTU 1 each, 600,000 BTU 2 each 700,000 BTU 1 each, 770,000 BTU | 
Function: | Heating work areas and equipment. | 
105

## Slide 135
Under Water Drop Lights |  |  |  | 
Quantity: | 10 Total |  |  | 
Manufacturer: | ACS, Deep Sea Power, and Keldan |  |  | 
Owner(s): | 6 each, ACS | 2 each, CPAI |  | 
 | 2 each, ENI |  |  | 
Specifications: | Sealed drop light designed for use in water |  |  | 
Function: | View oil pockets and movement under ice for winter recovery operations. |  |  | 
Auxiliary Equip: | Generator |  |  | 
106

## Slide 136
Light Plants and Stands |  |  |  | 
Quantity: | 50 Total |  |  | 
Manufacturer: | Hubbel-Cat, Allmand, Allman Bros., Bemis, Construction Electrical, Defender, Fostoria, Great Land Welding, Hubble-Cat, and Pelican |  |  | 
Owner(s): | 28 each, ACS |  | 7 each, CPAI | 6 each, ENI
 | 8 each, HAK |  | 1 each, Savant | 
Specifications: | 6 each, 2 light stands (500W) 18 each, 1 light stands (1,000W) 2 each, 2 light (1,000W) with tripod 1 each, 3 light stand (1,500W) 8 each, 2 light stands (2,000W) 1 each, 1 light stand (LED 16W) 2 each, 2 light stands (LED 70W) 1 each, 1 light stand (LED 72W) 1 each, 4 light stand (LED 96W) 7 each, 4 light stand (LED 200W) 2 each, light plant w/tracks (4,000W) 1 each, light plant (5,000W) |  |  | 
Function: | Illumination for night time response operations. |  |  | 
Auxiliary Equip: | Generator, extension cord |  |  | 
107

## Slide 137
Diesel Generators (various) |  |  |  | 
Quantity: | 64 Total |  |  | 
Manufacturer: | Alaska Diesel Electric, Cummins, Cummins Power Generation, Diesel America West, Equipment Source Inc., F.G. Wilson, Ingersoll Rand, KEM Equipment, Kubota, Magnum Products LLC., Norther Lights, Onan, and Pacific Detroit Diesel |  |  | 
Owner(s): | 34 each, ACS |  | 21 each, CPAI | 
 | 9 each, HAK |  |  | 
Specifications: | 10-2 kw, 6-3 kw, 14-4 kw, 3-5 kw, 9-6 kw, 1-9kw, 7-10 kw, 1-12 kw, 1-15 kw, 2-17 kw, 2-25 kw, 2-40 kw, 3-45 kw, 1-60 kw, 1-70 kw, 1-200kw |  |  | 
Function: | Electrical power for various pieces of response equipment. |  |  | 
Auxiliary Equip: | Power Splitter |  |  | 
108

## Slide 138
Gas Generators (various) |  |  |  | 
Quantity: | 56 Total |  |  | 
Manufacturer: | Honda, Powermate, and Yamaha |  |  | 
Owner(s): | 16 each, ACS |  | 16 each, CPAI | 
 | 4 each, ENI |  | 20 each, HAK | 
Specifications: | 4-1 kw, 22-2 kw, 19-3 kw, 6-4 kw, 2-5 kw, 3-7 kw |  |  | 
Function: | Electrical power for various pieces of response equipment. |  |  | 
109

## Slide 139
Air Compressors |  |  | 
Quantity: | 14 Total |  | 
Manufacturer: | Atlas Copco, Dayton, Devilbiss, Dewalt, Diesel America West, Ingersoll Rand, Maxus, Napa, Speedaire, and Sullair |  | 
Owner(s): | 2 each, (diesel), ACS |  | 2 each, (diesel), HAK
 | 1 each (gasoline), HAK |  | 
 | 6 each, (electric), ACS |  | 3 each, (electric) CPAI
Specifications: | 60 - 185 CFM |  | 
Function: | Provide industrial air service for response activities. |  | 
Auxiliary Equip: | Air hose |  | 
110

## Slide 140
06’, 10’, 20’ and 40’ Connex |  |  | 
Quantity: | 447 Total |  | 
Manufacturer: | Various |  | 
Owner(s): | 26 each, 06’ ACS |  | 
 | 2 each, 10’ ACS | 3 each, 10’ HAK | 
 | 192 each, 20’ ACS | 72 each, 20’ CPAI | 19 each, 20’ ENI
 | 86 each, 20’ HAK | 4 each, 20’ Savant | 
 | 5 each, 40’ ACS | 12 each, 40’ CPAI | 
 | 10 each, 40’ ENI | 16 each, 40’ HAK | 
Specifications: | 26 each, 06’ connex 5 each, 10’ connex 373 each, 20’ connex 43 each, 40’ connex |  | 
Function: | Material or boom storage. |  | 
111

## Slide 141
Portable Fuel Tanks |  |  |  | 
Quantity: | 16 Total |  |  | 
Manufacturer: | Greer Tank, Western International, and West-Mark |  |  | 
Owner(s): | 9 each, ACS | 5 each, CPAI |  | 
 | 2 each, HAK |  |  | 
Specifications: | 2 each, 100 gallons 1 each, 300 gallons 13 each, 500 gallons |  |  | 
Function: | Fueling support for either gasoline or diesel engines. |  |  | 
112

## Slide 142
This page intentionally left blank.

## Slide 143
Communications
Section H

## Slide 144
This page intentionally left blank.

## Slide 145
Portable Communications Towers |  | 
Quantity: | 1 Total | 
Manufacturer: | Aluma Tower Company | 
Owner(s): | ACS | 
Specifications: | 75’ Tower | 
Function: | Daily and oil spill response communications. | 
113

## Slide 146
Portable Communications Shelters |  | 
Quantity: | 2 Total | 
Manufacturer: | Vertex Plastics | 
Owner(s): | ACS | 
Function: | Transportation of communications shelter to be used for expansion of oil spill radio channel coverage. | 
Auxiliary Equip: | 4.0 kw diesel generator and 18’ trailer | 
114

## Slide 147
Handheld Radios |  |  |  | 
Quantity: | 296 Total |  |  | 
Manufacturer: | ICOM and Motorola |  |  | 
Owner(s): | 251 each, ACS | 42 each, CPAI |  | 
 | 1 each, ENI | 2 each, HAK |  | 
Specifications: | 24 each, UHF - ACS 23 each , UHF - CPAI 12 each, Harmony - ACS 211 each, VHF - ACS 19 each, VFH - CPAI 4 each, VHF marine - ACS 1 each VHF marine - ENI 2 each, VHF marine - HAK |  |  | 
Function: | Daily and oil spill response communications. |  |  | 
Auxiliary Equip: | Charger, repeater, gap filler and translator |  |  | 
115

## Slide 148
Iridium Phones |  | 
Quantity: | 22 Total | 
Manufacturer: | Beam Communications, Iridium, and Motorola | 
Owner(s): | ACS | 
Specifications: | 3 each, marine 19 each, handheld | 
Function: | Satellite telephone communications/internet and e-mail capabilities. | 
Auxiliary Equip: | Chargers, external antenna, SIMMS card | 
116

## Slide 149
Mobile Radios |  |  | 
Quantity: | 201 Total |  | 
Manufacturer: | General Electric, ICOM, and Motorola |  | 
Owner(s): | 163 each, ACS | 12 each, CPAI | 
 | 1 each, ENI | 25 each, HAK | 
Specifications | 3 each, UHF - ACS |  | 
 | 131 each, VHF - ACS | 10 each, VHF - CPAI | 
 | 15 each, VHF - HAK |  | 
 | 29 each, VHF marine - ACS | 2 each, VHF marine - CPAI | 
 | 1 each, VHF marine - ENI | 10 each, VHF marine - HAK | 
Function: | Marine, daily and oil spill response communications. |  | 
117

## Slide 150
GPS |  |  |  | 
Quantity: | 150 Total |  |  | 
Manufacturer: | Furuno, Garmin, Lowrance, Motorola, North Star, and Raymarine |  |  | 
Owner(s): | 63 each, ACS | 19 each, CPAI |  | 
 | 5 each, ENI | 63 each, HAK |  | 
Specifications: | Marine/handheld/plotter/GPS, radar Handheld 77 Marine 73 |  |  | 
Function: | Navigation and delineation. |  |  | 
Auxiliary Equip: | AA batteries, mag mount antenna |  |  | 
118

## Slide 151
Gap Fillers |  | 
Gap Filler |  | Translator
Quantity: | 6 Total | 
Manufacturer: | Codan Radio Communications and Daniels | 
Owner(s): | ACS | 
Specifications: | 4 each, repeaters 2 each, translators | 
Function: | Extend radio coverage. | 
Auxiliary Equip: | 12 volt automotive battery | 
119

## Slide 152
Radio Winter Drilling Kits |  | 
Quantity: | 11 Total Kits | 
Manufacturer: | ACS | 
Owner(s): | ACS | 
Specifications: | Per Kit: 3 each, VHF handhelds | 
 | Per Kit: 1 each, VHF mobile | 
 | Per Kit: 1 each, cellular bag phone | 
Function: | Communications kit for remote drilling support. | 
Auxiliary Equip: | Charger, mag mount antenna and spare batteries | 
120

## Slide 153
Wildlife
Section I

## Slide 154
This page intentionally left blank.

## Slide 155
Pinniped Enclosure |  |  |  | 
Quantity: | 2 Total |  |  | 
Manufacturer: | Alaska Sea Life Center |  |  | 
Owner(s): | ACS |  |  | 
Specifications: | 15’ Diameter x 4’ High |  |  | 
Function: | Storage area for captured Pinniped. |  |  | 
121

## Slide 156
Bear Cages and Transport Cages |  |  |  | 
Quantity: | 9 Total |  |  | 
Manufacturer: | Carter2systems (C2S1), Eton Welding & Machine, Homemade, Impact Dog Crates, Knapp, and Teton Welding & Manufacturing |  |  | 
Owner(s): | 5 each, ACS | 1 each, CPAI |  | 2 each, HAK
 | 1 each, US Fish and Wildlife |  |  | 
Specifications: | 1 each, 3 piece unit 2 each, trailer mounted unit 1 each, single cage 5 each, transport cage (2 each, Aircraft Compliant) |  |  | 
Function: | Storage area for captured bear. |  |  | 
122
3 piece unit
Transport cage, Aircraft Compliant

## Slide 157
Net Launchers |  |  |  | 
Quantity: | 4 Total |  |  | 
Manufacturer: | Coda Enterprises and Winchester |  |  | 
Owner(s): | 1 each, ACS | 1 each, CPAI | 1 each, ENI | 1 each, HAK
Specifications: | .308 Winchester shell/blank for launching net |  |  | 
Function: | Capture wildlife. |  |  | 
Auxiliary Equip: | .308 Blanks and net |  |  | 
123

## Slide 158
Wildlife Kits (capture and hazing) |  |  |  | 
Quantity: | 27 Total |  |  | 
Manufacturer: | Alaska Clean Seas |  |  | 
Owner(s): | 20 each, (hazing and capture ) ACS |  | 3 each, (hazing) CPAI | 
 | 1 each, (hazing) ENI |  | 3 each, (hazing) HAK | 
Specifications: | 17 each, wildlife hazing kits 10 each, capture kits |  |  | 
Function: | Capture contaminated wildlife for rehabilitation and haze animals away from contaminated areas. |  |  | 
124

## Slide 159
PepperBall Gun |  |  |  | 
Quantity: | 1 Total |  |  | 
Manufacturer: | PepperBall |  |  | 
Owner(s): | ACS |  |  | 
Specifications: Function: | Variable Kinetic System (VKS) Wildlife hazing |  |  | 
Auxiliary Equip: | Inert and Marking PepperBall, air tank, hopper |  |  | 
125

## Slide 160
12 Gauge Shot Guns |  |  |  | 
Quantity: | 21 Total |  |  | 
Manufacturer: | Benelli, New England Firearms, and Remington |  |  | 
Owner(s): | 13 each, ACS | 7 each, CPAI |  | 
 | 3 each, ENI |  |  | 
Specifications: | 9 each, New England Firearms single shot 12 each, Remington Model 870 pump 2 each, Benelli Nova Tactical |  |  | 
Function: | Wildlife hazing |  |  | 
Auxiliary Equip: | Cracker shells, rubber bullets, and slugs |  |  | 
126

## Slide 161
Bird Stabilization Center |  | 
Quantity: | 1 Total | 
Manufacturer: | Alaska Clean Seas | 
Owner(s): | ACS | 
Specifications: | 2 connecting units Each section is portable and can be moved individually by truck or C-130 | 
Function: | Decontamination and rehabilitation of wildlife. The construction of the center enables it to be transported to any location on or off the North Slope. | 
127

## Slide 162
Bird Scare Devices |  |  |  |  | 
Quantity: | 70 Total |  |  |  | 
Manufacturer: | Bird Gard, Breco, Dazon BV Maastricht, Feather-Light Tech, and Reed Joseph |  |  |  | 
Owner(s): | 46 each, propane, ACS |  |  |  | 7 each, propane, CPAI
 | 2 each, propane, ENI |  |  |  | 3 each, propane, HAK
 | 11 each, electronic, HAK 1 each, laser, HAK |  |  |  | 
Specifications: | 58 each, propane cannons 1 each, laser 11 each, electronic |  |  |  | 
Function: | Wildlife hazing. |  |  |  | 
Auxiliary Equip: | Propane tank and receiver unit for electronic units. Battery for testing. |  |  |  | 
128

## Slide 163
Miscellaneous
Section J

## Slide 164
This page intentionally left blank.

## Slide 165
De-Icer |  |  | 
Quantity: | 2 Total |  | 
Manufacturer: | Kasco |  | 
Owner(s): | ACS |  | 
Specifications: | Model 4400D 1 HP |  | 
Function: | De-icers push warm bottom water to the surface creating an ice-free area. |  | 
Auxiliary Equip: | Generator, line |  | 
129

## Slide 166
Ground Penetrating Radar System |  |  | 
Quantity: | 1 Total |  | 
Manufacturer: | Sensors & Software Inc. |  | 
Owner(s): | ACS |  | 
Specifications: | Model Pulse EKKO Pro |  | 
Function: | Ice profiling, determination of ice thickness and detection of spilled oil under ice |  | 
Auxiliary Equip: | (2) Transmitter and receiving units |  | 
130

## Slide 167
Hydraulic Power Units (various) |  |  |  |  |  |  |  | 
Quantity: |  | 154 Total |  |  |  |  |  | 
Manufacturer: |  | Various |  |  |  |  |  | 
Owner(s): |  | 74 each, ACS |  | 31 each, CPAI |  |  |  | 
 |  | 8 each, ENI |  | 41 each, HAK |  |  |  | 
Specifications: |  | Varies for purpose |  |  |  |  |  | 
Function: |  | Power boom deployment and recovery systems. |  |  |  |  |  | 
Auxiliary Equip: |  | Hydraulic hoses and possibly remote controller |  |  |  |  |  | 
131

## Slide 168
MegaSecur Dams |  |  | 
Quantity: | 8 Total |  | 
Manufacturer: | MegaSecur Water-Gate, Models WA2825, WA2850, and WA3950 |  | 
Owner(s): | 4 each, 25’, HAK 2 each, 50’, ACS |  | 1 each, 30’, HAK 1 each, 50’, HAK
Specifications: | 25’ x 28” 30’ x 39” 50’ x 28” 50’ x 39” |  | 
Function: | Water gate to slow current in small streams to aid in recover operations. |  | 
Accessories: | PVC pipe can be placed under dam to create an underflow dam |  | 
132

## Slide 169
MetOcean Spill Tracking Systems |  |  | 
Tracking Buoy |  | Ice Beacon Housing | 
Quantity: | 12 Total |  | 
Manufacturer: | MetOcean |  | 
Owner(s): | 6 each, Tracking Buoy, ACS |  | 
 | 4 each, Tracking Buoy, ENI |  | 
 | 2 each, Tracking Buoy, CPAI |  | 
 | 8 each, Ice Beacon Housing, ACS |  | 
Specifications: | iSphere Drift Buoy – Iridium Satellite Communications |  | 
Function: | Tracking oil spills in offshore currents and broken ice conditions. |  | 
Auxiliary Equip: | Computer and software |  | 
133

## Slide 170
Underwater ROV |  |  | 
Quantity: | 1 |  | 
Manufacturers: | Chasing |  | 
Owner: | ACS |  | 
Specifications: | Capable of 490’ diving depth at 4 knots 4k video camera Tether provides constant power source – battery alone lasts 4 hours |  | 
Function: | Video surveillance and documentation of oil spills. Vessel hull and underwater pipeline inspection, underwater oil spill investigation. |  | 
Auxiliary Equip: | 2000 lumen light, grabber arm |  | 
134

## Slide 171
Unmanned Aircraft Systems |  |  | 
Quantity: | 5 Total (Four rotary, one fixed wing) |  | 
Manufacturers: | Yuneec, DJI, Autel Robotics, FOX TECH |  | 
Owner: | ACS |  | 
Specifications: | Yuneec H520: One-half hour flight time, 160 thermal and 4K video cameras. Mavic 2 Pro: One- half hour flight time, 4k video camera. Autel Robotics Evo II Dual MDCD: One-half hour flight time, 640 thermal sensor combined with 8k/48MP visual camera. FOX TECH Great Shark: Vertical take off and land, 2.5 hours flight time, beyond visual line of sight capabilities and 4k video with 30x zoom. |  | 
Function: | Video surveillance and documentation of oil spills. Shoreline assessment, wildlife surveillance, on water oil spotting. |  | 
Auxiliary Equip: | Extra batteries for all to enable unlimited flight time. |  | 
135

## Slide 172
This page intentionally left blank.

## Slide 173
This page intentionally left blank.

## Slide 174
CONTACT INFORMATION
24 – Hour Emergency Number
(907)659-2405
www.alaskacleanseas.org
Anchorage Office:
Alaska Clean Seas
3300 C St. Suite 200
Anchorage, AK 99503
Phone: (907) 743-8989
Fax: (907) 743-8988
North Slope Office:
Alaska Clean Seas
P.O. Box 340022
Prudhoe Bay, AK 99734
Phone: (907) 659-2405
Fax: (907) 659-2616